## Slide 1
AUTONOMOUS INTELLIGENT SYSTEMS
···
···
VOICE RECOGNITION FOR ROBOT CONTROL
VRC — 4
Khushal Singh (1564813) · Raka Sarkar(1567153) · Taibaz Pathan(1564714)
Under the guidance of Prof. Dr. Peter Nauth
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems

## Slide 2
02
MOTIVATION & OBJECTIVES
Why Voice-Controlled Robot Navigation?
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
Hands-Free Control
Enable intuitive, hands-free navigation of a robot in a lab environment — no specialised controllers required.
ROS 2 Integration
Integrate a fully offline speech pipeline with the ROS 2 middleware and Gazebo physics simulation.
End-to-End Pipeline
Demonstrate a complete pipeline: audio input → ASR → intent classification → safety gate → robot motion.
Reusable Framework
Deliver a modular, configurable framework reusable for future student projects beyond navigation.

## Slide 3
03
SYSTEM OVERVIEW
Five-Node ROS 2 Pipeline
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
AudioInput
Node
/audio/raw
▶
ASR
Node
/asr/text
▶
Intent
Node
/asr/intent
▶
StateMachine
Node
/voice/command
▶
Command
Node
/cmd_vel
Node | Subscribes | Publishes | Responsibility
AudioInputNode | /— | /audio/raw | Injects WAV file paths at 5 s intervals for deterministic evaluation
ASRNode | /audio/raw | /asr/text | Normalise → VAD → Whisper small int8; publishes if conf ≥ 0.40
IntentNode | /asr/text | /asr/intent | RapidFuzz fuzzy match; threshold 75; min(ASR_conf, fuzzy_score)
StateMachineNode | /asr/intent | /voice/command | IDLE→WAITING→EXECUTING FSM; YES/NO gate; 5 s timeout; emergency STOP
CommandNode | /voice/command | /cmd_vel | Translates commands to geometry_msgs/Twist at 10 Hz

## Slide 4
04
ASR MODULE
Voice Processing Pipeline
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
FRANKFURT UNIVERSITY OF APPLIED SCIENCES
1
Normalise + VAD
Mono → 16 kHz resample → peak normalise. Fixed RMS threshold 0.01 on 20 ms frames removes silence. Adaptive VAD was prototyped but reverted — Edge TTS mean-RMS caused regression.
threshold = 0.01
2
Whisper Transcription
faster-whisper small int8 on CPU. initial_prompt primes decoder to the 5-command vocabulary — this was the key improvement: raised noisy accuracy from 73% → 97.3%.
initial_prompt = "move forward..."
3
Confidence Score
conf = min(1.0, exp(mean_avg_logprob)). Whisper small short-command logprobs map to conf in [0.37, 0.61]. Operational threshold set at 0.40 (not original 0.75).
threshold = 0.40

## Slide 5
05
INTENT & SAFETY
Intent Classification + Safety State Machine
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
FRANKFURT UNIVERSITY OF APPLIED SCIENCES
Intent Module
Vocabulary
5 commands: move forward/backward, turn left/right, stop
Fuzzy Match
RapidFuzz weighted ratio — threshold 75/100 (raised from 60 to prevent 'turn light'→'turn right' at 67)
Confidence
conf_final = min(conf_ASR, fuzzy_score/100)
Gate
conf_final < 0.40 → NO_COMMAND silently rejected
Safety State Machine (FSM)
IDLE
WAITING_CONFIRMATION
EXECUTING (transient)
valid cmd, conf≥0.40
"yes" confirmed
"no" / timeout 5s → back to IDLE
⚡ Emergency STOP: conf > 0.90 → bypass confirmation → execute immediately

## Slide 6
06
ROS 2 NODE
Node 1 – AudioInputNode → Node 2 – ASRNode
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
FRANKFURT UNIVERSITY OF APPLIED SCIENCES
AudioInputNode
Python / rclpy
pub → /audio/raw
▸ Injects pre-recorded WAV paths at 5 s intervals
▸ File injection ensures fully deterministic, repeatable evaluation
▸ No microphone hardware dependency
▸ Enables full 400-sample batch testing without manual input
ASRNode
asr_module.asr_engine
sub ← /audio/raw
pub → /asr/text
▸ Normalise → VAD (0.01 threshold) → Whisper small int8
▸ initial_prompt biases decoder to 5-command vocabulary
▸ conf = min(1.0, exp(mean_avg_logprob)) — gate at 0.40
▸ normalize_text() fixes Whisper phonetic substitution errors

## Slide 7
07
ROS 2 NODE
Node 5 – CommandNode: Voice-to-Motion Mapping
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
FRANKFURT UNIVERSITY OF APPLIED SCIENCES
CommandNode
sub ← /voice/command
pub → /cmd_vel
▸ Translates command tokens to geometry_msgs/Twist
▸ Publishes velocity at 10 Hz for duration, then sends zero-velocity stop
▸ Safety: stop dispatched immediately (bypass timer)
Command | linear.x (m/s) | angular.z (rad/s) | Duration
move forward | +0.3 | 0.0 | 2.0 s
move backward | −0.3 | 0.0 | 2.0 s
turn left | 0.0 | +0.5 | 1.5 s
turn right | 0.0 | −0.5 | 1.5 s
stop | 0.0 | 0.0 | immediate
Published at 10 Hz via /cmd_vel · Zero-velocity Twist sent after duration to stop robot

## Slide 8
08
GAZEBO ENVIRONMENT
Robot Model and Simulation World
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
Custom URDF Humanoid
Base, pelvis, torso, head, arms, eyes, mouth — plus differential drive wheel base (ROSWITHA model)
Differential Drive
Wheels linked via left_wheel_joint and right_wheel_joint — gazebo_ros_diff_drive plugin with wheel separation & radius
Gazebo Plugin
gazebo_ros_diff_drive configured; subscribes to /cmd_vel; converts velocity commands to wheel rotations
University Lab World
Floor, walls, blackboard, laptop desks, stool, equipment cart, props — realistic indoor lab environment
Camera Setup
Viewpoint configured for clear observation of robot motion during evaluation; side and top-down views

## Slide 9
09
DATA FLOW
ROS 2 Topic-Level Data Flow — Full 5-Node Pipeline
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
FRANKFURT UNIVERSITY OF APPLIED SCIENCES
AudioInput
Node
/audio/raw
▶
ASR
Node
/asr/text
▶
Intent
Node
/asr/intent
▶
StateMachine
Node
/voice/command
▶
Command
Node
/cmd_vel
Gazebo
diff_drive
▶
All components loosely coupled via ROS 2 topics — any node can be replaced independently (e.g. swap ASR engine, add live microphone node, upgrade to navigation stack).
Key Topics:
/audio/raw — String (WAV path) · /asr/text — String (transcript + conf) · /asr/intent — String (intent token) · /voice/command — String (confirmed cmd) · /cmd_vel — geometry_msgs/Twist

## Slide 10
10
EVALUATION
Dataset: 400 Samples · 20 Speakers · 4 Conditions
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
FRANKFURT UNIVERSITY OF APPLIED SCIENCES
400
Total Samples
100 clean + 300 noisy
20
Accent Profiles
American, British, Indian,
Australian, Nigerian + 10 more
3
SNR Noise Levels
20 dB / 10 dB / 0 dB
(equal signal & noise power)
20
OOV Utterances
False activation test
5 voices, 20 phrases
Speakers | Edge TTS Voices | Accent | Samples
spk 1–2 | en-US-Guy / en-US-Jenny | American M/F | 20
spk 3–4 | en-GB-Ryan / en-GB-Sonia | British M/F | 20
spk 5–6 | en-IN-Neerja / en-IN-Prabhat | Indian F/M | 20
spk 7–8 | en-AU-William / en-AU-Natasha | Australian M/F | 20
spk 9–20 | Nigerian, Irish, S.African, Canadian, NZ, Singaporean, Kenyan, Filipino | Various M/F | 240

## Slide 11
11
RESULTS
All KPIs Met or Exceeded
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
FRANKFURT UNIVERSITY OF APPLIED SCIENCES
99.0%
+14 pp
Clean Accuracy
99/100 · Target >85%
97.3%
+27 pp
Noisy Accuracy
292/300 · Target >70%
0.0%
Perfect
False Activations
0/20 OOV · Target <2%
1.55s
3.2× margin
Mean Latency
noisy set · Target <5s
Per Noise Condition
Condition | Correct | Accuracy | Target
Clean | 99/100 | 99.0% | >85% ✓
SNR 20 dB | 97/100 | 97.0% | >70% ✓
SNR 10 dB | 98/100 | 98.0% | >70% ✓
SNR 0 dB | 97/100 | 97.0% | >70% ✓
Per Command
Command | Clean | Noisy
move forward | 100% | 100%
move backward | 100% | 96.7%
turn left | 100% | 100%
turn right | 100% | 100%
stop | 95.0% | 90.0%

## Slide 12
12
CHALLENGES
Key Engineering Challenges & Solutions
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems
Problem:
Confidence threshold 0.75 blocked all commands
Root cause: Whisper small short-command logprobs → exp(avg_logprob) in [0.37, 0.61]. At 0.75, 97% of valid commands rejected.
✓ Solution: Calibrated threshold to 0.40 using confidence distribution of 300 noisy samples. [0.40, 0.75) bucket: 99.4% accuracy.
Problem:
Adaptive VAD caused accuracy collapse
Root cause: mean_RMS × 1.5 ceiling of 0.05 trimmed valid speech. Edge TTS audio has higher mean RMS than human speech → SNR 10/20 dB regression from 88% → 43%.
✓ Solution: Reverted to fixed threshold = 0.01. Stable across all 20 speakers and all 3 SNR levels.
Problem:
log_prob_threshold = −0.5 zeroed confidence on clean audio
Root cause: Whisper per-token logprobs for short 1–2 word commands fall below −0.5 normally (exp(−0.5) ≈ 0.61). All clean samples returned conf = 0.0.
✓ Solution: Reset to −2.0 (effectively disabled). Downstream confidence gate at 0.40 handles rejection without suppressing valid segments.

## Slide 13
13
CONCLUSIONS & FUTURE WORK
Summary & Outlook
✓ Conclusions
▸ All 5 KPIs met or exceeded — 99% clean, 97.3% noisy, 0% FAR, 1.55s latency, 100% safety
▸ faster-whisper small int8 achieves real-time-adjacent ASR on CPU without GPU or cloud dependency
▸ initial_prompt was the decisive improvement: raised noisy accuracy from 73% → 97.3%
▸ Safety FSM prevents any unconfirmed robot motion; emergency STOP bypasses confirmation at conf > 0.90
▸ 20-accent, 400-sample corpus demonstrates strong speaker independence
→ Future Work
▸ Live microphone node with real-time streaming VAD
▸ Physical ROSWITHA / TurtleBot deployment under real acoustic conditions
▸ Vocabulary expansion with re-calibrated fuzzy threshold
▸ Whisper fine-tuning on robotics commands for underperforming accents (Indian Female, spk4 stop)
▸ Platt scaling for calibrated confidence estimates from log-probability proxy
Clean 99.0% · SNR 0dB 97.0% · SNR 10dB 98.0% · SNR 20dB 97.0% · FAR 0.0% · Latency 1.55s · Safety 5/5 ✓ All KPIs Passed
M.Eng. Information Technology / WS 25-26 / Autonomous Intelligent Systems